## Slide 1
Tutorial
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 2: Mission Statement
ZigBee Alliance members are defining global standards for reliable, cost-effective, low power wireless applications. The ZigBee Alliance is a rapidly growing, non-profit industry consortium of leading semiconductor manufacturers, technology providers, OEMs and end users worldwide.
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 3: Development of the Standard
IEEE 802.15.4 Working Group
  Defining lower layers of protocol stack: MAC and PHY
  Available today
ZigBee Alliance
  50+ companies: semiconductor mfrs, IP providers, OEMs, etc.
  Defining upper layers of protocol stack: from network to application, including application profiles
  Initial draft available mid 2003
SILICON
ZIGBEE STACK
APPLICATION
Customer
IEEE
ZigBee
Alliance
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 4: The ZigBee Alliance Solution
Targeted at home and building automation and controls, consumer electronics, PC peripherals, medical monitoring, and toys
Industry standard through application profiles
Primary drivers are simplicity, long battery life, networking capabilities, reliability, and cost
Alliance provides interoperability and certification testing
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 5: History
ZigBee
IEEE 802.15.4
1998
1999
2000
2001
2002
RSI/TRD
Proposals
Initial MRD
v0.2
PAR
Proposal
to IEEE
Proposals
Completion
Reviews
ZigBee Alliance
formed
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 6: The Wireless Market
SHORT < RANGE > LONG
LOW < DATA RATE > HIGH
PAN
LAN
TEXT
GRAPHICS
INTERNET
HI-FI
AUDIO
STREAMING
VIDEO
DIGITAL
VIDEO
MULTI-CHANNEL
VIDEO
Bluetooth1
ZigBee
802.11b
802.11a/HL2 & 802.11g
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 7: Applications
ZigBee
LOW DATA-RATE
RADIO DEVICES
HOME AUTOMATION
CONSUMER ELECTRONICS
TV
VCR
DVD/CD
remote
security
HVAC
lighting
closures
PC & PERIPHERALS
TOYS &
GAMES
consoles portables
educational
PERSONAL HEALTH CARE
INDUSTRIAL & COMMERCIAL
monitors
sensors
automation
control
mouse
keyboard
joystick
monitors
diagnostics
sensors
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 8: Market Requirements (1)
Global, license free ISM band operation
Unrestricted geographic use
RF penetration through walls & ceilings
Automatic/semi-automatic installation
Ability to add or remove devices
Cost advantageous
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 9: Market Requirements (2)
10k-115.2kbps data throughput
10-75m coverage range
Up to 65k slave nodes per network
Up to 100 co-located networks
Up to 2 years of battery life on standard Alkaline batteries
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 10: Frequencies and Data Rates
BAND COVERAGE DATA RATE CHANNEL(S)
2.4 GHz ISM Worldwide 250 kbps 11-26
868 MHz Europe 20 kbps 0
915 MHz ISM Americas 40 kbps 1-10
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 11: Stack Reference Model
IEEE 802.15.4 PHY
IEEE 802.15.4 MAC (CPS)
ZigBee NWK
MAC (SSCS)
802.2 LLC
IP
API
UDP
ZA1
ZA2
…
ZAn
IA1
IAn
Transmission & reception on the physical radio channel
Channel access, PAN maintenance, reliable data transport
Topology management, MAC management, routing, discovery protocol, security management
Application interface designed using
general profile
End developer applications, designed using application profiles
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 12: Protocol Stack Features
8-bit microcontroller
Full protocol stack <32 k
Simple node-only stack ~4k
Coordinators require extra RAM
  Node device database
  Transaction table
  Pairing table
PHY LAYER
MAC LAYER
MAC LAYER
DATA LINK LAYER
NETWORK LAYER
APPLICATION INTERFACE
APPLICATION
Silicon
ZigBee Stack
Application
Customer
IEEE
ZigBee
Alliance
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 13: Topology Models
PAN coordinator
Full Function Device
Reduced Function Device
Star
Mesh
Cluster Tree
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 14: IEEE 802.15.4 MAC Overview
Employs 64-bit IEEE & 16-bit short addresses
One PAN coordinator & multiple RFDs/FFDs
Optional superframe structure with beacons
CSMA-CA channel access
Simple frame structure
Reliable delivery of data
Association/disassociation
GTS mechanism
AES-128 security
Δρ. Γεώργιος Δημητρακόπουλος

## Slide 15: More Information
ZigBee Alliance web site http://www.ZigBee.org
IEEE 802.15.4 web site
  http://www.ieee802.org/15/pub/TG4.html
Δρ. Γεώργιος Δημητρακόπουλος